## Slide 1: A Two Level Neural Approach Combining Off-Chip Prediction with Adaptive Prefetch Filtering
Alexandre Valentin Jamet1
1Barcelona Supercomputing Center
alexandre.jamet@bsc.es

## Slide 2: Executive Summary
Emerging workloads (e.g., graph processing) have massive data footprints
  Significant pressure on the caches
Latency Tolerance Techniques:
  Off-Chip Prediction (e.g., Hermes (MICRO’22))
  Data Prefetching (e.g., PPF (ISCA’19))
  Cache bypassing (e.g., Multiperspective Reuse Prediction (MICRO’17))
  Disruptive cache designs (e.g., Distill Cache (HPCA’07))
Notes: Quickly span through the problem of modern workloads (i.e., large data footprint).
Then, go on to explaining the different techniques available to workaround these problems:
Off-Chip Prediction (Predicting load demand accesses for cache hits)
Data Prefetching coupled with Adaptive Filtering (Improving prefetching for adaptive workload handling)
Cache bypassing (Selective bypass strategies for system performance)
Disruptive cache designs (Innovative architectures for efficiency and performance)

## Slide 3: Executive Summary
Emerging workloads (e.g., graph processing) have massive data footprints
  Significant pressure on the caches
Latency Tolerance Techniques:
  Off-Chip Prediction (e.g., Hermes (MICRO’22))
  Data Prefetching (e.g., PPF (ISCA’19))
  Cache bypassing (e.g., Multiperspective Reuse Prediction (MICRO’17))
  Disruptive cache designs (e.g., Distill Cache (HPCA’07))
Limitations in Off-Chip Prediction mechanisms:
    Balancing speed-up with increased DRAM transactions
    Adaptability issues in prefetch filtering approaches
Our approach
  Make Off-Chip prediction highly accurate
  We leverage Off-Chip prediction properties to drive Adaptive Prefetch Filtering
Notes: Quickly span through the problem of modern workloads (i.e., large data footprint).
Then, go on to explaining the different techniques available to workaround these problems:
Off-Chip Prediction (Predicting load demand accesses for cache hits)
Data Prefetching coupled with Adaptive Filtering (Improving prefetching for adaptive workload handling)
Cache bypassing (Selective bypass strategies for system performance)
Disruptive cache designs (Innovative architectures for efficiency and performance)

## Slide 4: Cache Behaviour of Modern Workloads
For SPEC and GAP workloads, we analyse the load in the cache hierarchy
On average, 34.7% of L1D misses eventually require a DRAM access
  Graph workloads exhibit irregular access pattern that caches can hardly capture
Most demand load requests triggered by applications with large working set sizes miss in all cache levels.
Notes: Here, we mention that modern workloads (and particularly GAP) put large load on the cache hierarchy.

## Slide 5: Off-Chip Prediction
Assess whether a load demand access will be served from the caches or the DRAM
Promising technique. No yet implemented by leading vendors
A state-of-the-art design is Hermes (MICRO’22)
CORE
L1D
L2C
LLC
DRAM
Throw a speculative request to DRAM?
Notes: Here, we give a brief explanation on what is Off-Chip prediction
Basically, a predictor figures out whether or not a load demand access originating from the core would require a DRAM access or hit somewhere in the cache hierarchy?
If predicted off-chip, in addition to the regular memory access from the core, a prefetch request to the DRAM is issued. If not, the regular memory access process is followed.

## Slide 6: Limitations of Off-Chip Prediction
Hermes provides performance benefits
  Single-core —> 5.2% geomean speed-up
  Multi-core —> 11.5% geomean speed-up
Hermes significantly increases the # of DRAM transactions
  Single-core —> 6.4% on average
  Multi-core —> 6.0% on average
Hermes significantly increases DRAM accesses (both single-core and multi-core contexts).
Notes: Here, we show the limitations of Hermes (i.e., while Hermes provides speed-up, it also increases the # of DRAM transactions).
Fine if we are dealing with a system with large resources but in practice completely impractical.

## Slide 7: Limitations of Off-Chip Prediction
Measuring Hermes’ inaccurate off-chip predictions:
  42.2% of off-chip predictions are inaccurate —> hit in cache hierarchy
  17.7% of total off-chip predictions are found in the L1D.
Selectively delaying Hermes off-chip predictions until the L1D lookup is resolved has the potential to significantly reduce the number of useless DRAM transactions and deliver performance.
Notes: Here, we demonstrate that 42.2% of Hermes’ off-chip predictions are inaccurate (i.e., while predicted off-chip, the requests are satisfied somewhere in the cache hierarchy).
Take way: It might pay off to wait to consume the prediction when we lack confidence at the core level. The idea being that with L1D misses we leverage an additional information that skews towards off-chip.

## Slide 8: Hardware Prefetching & Prefetch Filtering
Prefetchers proactively fetch blocks into caches before they are demanded by the core
Not all prefetch requests are useful —> Need to filter useless prefetch requests
CORE
L1D
L2C
LLC
DRAM
PF
PF
PF
Is PFR useful?
Notes: Here we present the concept of hardware prefetching combined with adaptive prefetching.

## Slide 9: Hardware Prefetching & Prefetch Filtering
Where are useless (not touched during their lifetime) prefetches fetched from?
  L2C —> 18.2%
  LLC —> 3.8%
  DRAM —> 78%
On average 95.2% of prefetch requests served by the DRAM are inaccurate
Off-chip prediction can be leveraged to design an effective prefetch filtering scheme for L1D.
Notes: Here, we demonstrate that most of the useless prefetch request are served from DRAM, establishing a link between Adaptive Filtering for Hardware Prefetching and Off-Chip Prediction.

## Slide 10: TLP: A Solution to address useless DRAM Transactions
Selectively delaying Off-Chip predictions can reduce the # of DRAM transactions
  Improve Hermes to selectively delay speculative DRAM accesses after L1D misses
  We propose the First Level Perceptron (FLP)
Useless L1D prefetch requests are mostly fetched from DRAM
  Off-Chip prediction can drive Prefetch Filtering
  We propose the Second Level Perceptron (SLP)
Finally, we assemble FLP and SLP into the Two Level Perceptron (TLP)
We assemble FLP and SLP into the Two Level Perceptron (TLP).
Notes: Here we summarise the findings to transition to the design proposal.

## Slide 11: FLP: Leveraging Off-Chip Prediction for Prefetch Filtering
FLP is a hashed perceptron predictor
Utilizes several µ-arch features (history of load PCs, etc.)
  Components (5 prediction tables, 128-1K entries, history of the last n-load PCs, virtual address bits, etc.)
FLP is consulted upon a load demand request
Prediction outcomes:
  On-Chip —> No DRAM prefetch
  Off-Chip —> DRAM prefetch from the core
  Delayed Prediction —> Delays DRAM prefetch after L1D lookup
FLP is trained when a request returns to the core

## Slide 12: SLP: An Approach to Off-Chip Prediction-based Prefetch Filtering
SLP is a hashed perceptron predictor
Utilizes several µ-arch features (history of load PCs, etc.)
  Components (6 prediction tables, 128-1K entries, history of the last n-load PCs, physical address bits, output of FLP, etc.)
SLP is consulted upon a L1D prefetch request emission
Prediction outcomes:
  On-Chip —> the prefetch request is issued
  Off-Chip —> the prefetch request is discarded
Similarly to FLP, SLP is trained upon the completion of an L1D prefetch request.

## Slide 13: TLP: An Approach to Off-Chip Prediction-based Prefetch Filtering
The Two Level Perceptron (TLP) Predictor combines the FLP and the SLP
It allows a layered perceptron design
  SLP uses the output of the FLP as an input
❶ FLP provides confidence on a load going off-chip
High confidence triggers speculative DRAM request ❷
Low confidence delays DRAM request until L1D miss ❸
If predicted to be on-chip, no action taken ❹

## Slide 14: TLP: An Approach to Off-Chip Prediction-based Prefetch Filtering
SLP is consulted upon L1D prefetch requests ❺
If the request is predicted to be off-chip ❻, the request is discarded
If the request is predicted to be on-chip ❼, the request continues as usual
The Two Level Perceptron (TLP) Predictor combines the FLP and the SLP
It allows a layered perceptron design
  SLP uses the output of the FLP as an input

## Slide 15: Experimental Setup
ChampSim simulator (GitHub)
Cascade Lake micro-architecture (specs)
Workloads
  SPEC CPU 2006 & 2017 (24 workloads)
  GAP Benchmark Suite (31 workloads)
  SimPoints methodology
Single-core evaluation
Multi-core evaluation
Component | Parameters | Latency
ITLB | 64-entry, 4-way | 1cc
DTLB | 64-entry, 4-way | 1cc
STLB | 1536-entry, 12-way | 8cc
L1 I-Cache | 32KB, 8-way | 4cc
L1 D-Cache | 32KB, 8-way, IPCP/Berti Prefetcher | 4cc
L2 Cache | 1MB, 16-way, SPP Prefetcher | 10cc
LLC | 1.375MB/core, 11-way | 20cc
DRAM | 16GB, tRP=tRCD=tCAS=24cc | variable
Notes: Here, we simply describe the simulation set-up.

## Slide 16: Alternative Techniques
Designs evaluated:
  PPF (ISCA’19)
  Hermes (MICRO’22)
  Hermes+PPF
  TLP (our design)
Considered L1D Prefetchers:
  IPCP (ISCA’20)
  Berti (MICRO’22)
Hermes+PPF, like TLP provides Off-Chip Prediction and Adaptive Prefetch Filtering.
Notes: The alternative techniques we are considering.

## Slide 17: Single-Core Evaluation | Performance
Considering a single-core scenario, TLP outperforms all considered designs
  n.b., The single-core scenario assumes 12.8 GB/s per core of DRAM bandwidth
  n.b., We evaluated TLP over a range of DRAM bandwidth allocation. We observe that as bandwidth decreases, TLP’s potential grows higher
  TLP leverages 6.2% geomean speed-up as compared to -0.2%, 5.2%, and 4.7% for PPF, Hermes, and Hermes+PPF, respectively

## Slide 18: Single-Core Evaluation | DRAM Transactions
Considering a single-core scenario, TLP significantly reduces DRAM transactions as compared all considered designs
    TLP reduces DRAM transactions by 30.7% on average, while DRAM transactions increase by 7.7%, 5.2%, and 13.3% for PPF, Hermes, and Hermes+PPF, respectively

## Slide 19: Multi-Core Evaluation | Performance & DRAM Transactions
Considering a multi-core scenario, TLP outperforms all considered designs
  n.b., The multi-core scenario assumes 3.2 GB/s per core of DRAM bandwidth
  TLP leverages 11.5% geomean speed-up as compared to -3.3%, 3.0%, and -0.5% for PPF, Hermes, and Hermes+PPF, respectively
  TLP reduces DRAM transactions by 17.7% on average, while DRAM transactions increase by 6.5%, 6.0%, and 13.4% for PPF, Hermes, and Hermes+PPF, respectively

## Slide 20: Multi-Core Evaluation | Impact of Bandwidth
Considering a multi-core scenario, TLP outperforms all considered designs
  n.b., The x-axes measures bandwidth in GB/s per core.
  n.b., Here, we vary DRAM bandwidth from 1.6 to 25.6 GB/s per core.
  TLP outperforms all approaches in scenarios where bandwidth ranges between 1.6 to 6.4 GB/s per core
  Even considering unrealistic scenarios (12.8 and 25.6 GB/s per core), TLP outperforms Hermes and PPF

## Slide 21: Conclusions
We show that off-chip prediction can be used to drive prefetch filtering, reducing the # of DRAM transactions and ultimately improving performance.
This work generalises to any L1D prefetcher and/or workloads.
Off-chip prediction could be correlated to other µ-architectural problems (Dead-On-Arrival STLB entries, etc.).

## Slide 22: Reproducing results — Public Artifact
An artifact is publicly available for you to reproduce the results and play around.
  Main artifact on Zenodo.
We provide the traces used for the paper.
  Volume 1 on Zenodo.
  Volume 2 on Zenodo.
  Volume 3 on Zenodo.

## Slide 23: Thank you for your attention!
A Two Level Neural Approach Combining Off-Chip Prediction with Adaptive Prefetch Filtering — HPCA’24

## Slide 24: Acknoledgments/ Fundings
Alexandre Valentin Jamet acknowledges his AI4S fellowship within the “Generación D” initiative by Red.es, Ministerio para la Transformación Digital y de la Función Pública, for talent attraction (C005/24-ED CV1), funded by NextGenerationEU through PRTR.

## Slide 25: BACKUP SLIDES

## Slide 26: Details on Graph Workloads
 | BC | BFS | CC | PR | TC | SSP
irregData ElemSz | 8B + 4B | 4B | 4B | 4B | 4B | 4B
Execution style | Push-Mostly | Push & Pull | Push-Mostly | Pull-Only | Push-Only | Push-Only
Use Frontier | Yes | Yes | No | No | No | Yes
 | Web | Road | Twitter | Kron | Urand | Friendster
# Vertices (in M) | 50.6 | 23.9 | 61.6 | 134.2 | 134.2 | 65.2
# Edges (in M) | 1,949.4 | 58.3 | 1,468.4 | 2,111.6 | 2,147.4 | 3,612.1
Notes: Here, we simply describe the simulation set-up.

## Slide 27: Hardware Prefetching & Prefetch Filtering (Berti)
Where are useless (not touched during their lifetime) prefetches fetched from?
  L2C —> 18.2%
  LLC —> 3.8%
  DRAM —> 78%
On average 95.2% of prefetch requests served by the DRAM are inaccurate
  Worse on GAP workloads (96.7%) as compared to SPEC (82%).

## Slide 28: Single-Core Evaluation / Performance (Berti)
Considering a single-core scenario, TLP outperforms all considered designs.
  n.b., The single-core scenario assumes 12.8 GB/s per core of DRAM bandwidth. This favours aggressive prefetching techniques.
  TLP leverages 8.1% geomean speed-up as compared to 1.7%, 4.8%, and 6.1% for PPF, Hermes, and Hermes+PPF, respectively.

## Slide 29: Single-Core Evaluation / DRAM Transactions (Berti)
Considering a single-core scenario, TLP significantly reduces DRAM transactions as compared all considered designs.
    TLP reduces DRAM transactions by 14.2% on average, while DRAM transactions increase by 8.8%, 9.6%, and 16.9% for PPF, Hermes, and Hermes+PPF, respectively.

## Slide 30: Multi-Core Evaluation / Performance & DRAM Transactions (Berti)
Considering a multi-core scenario, TLP outperforms all considered designs.
  n.b., The multi-core scenario assumes 3.2 GB/s per core of DRAM bandwidth. The favours less aggressive prefetching techniques.
  TLP leverages 11.8% geomean speed-up as compared to -1.5%, 1.0%, and 0.3% for PPF, Hermes, and Hermes+PPF, respectively.
  TLP reduces DRAM transactions by 17.7% on average, while DRAM transactions increase by 6.5%, 6.0%, and 13.4% for PPF, Hermes, and Hermes+PPF, respectively.

## Slide 31: Performance contribution of each TLP component
We breakdown the the performance contribution of each building blocks of the final TLP proposal:
  FLP —> 2.9%
  SLP —> 6.9%
  TSP —> 8.4%
  Delayed TSP —> 10.2%
  Selective TSP —> 11.4%
  TLP —> 11.5%

## Slide 32: Enhanced designs with TLP’s budget
Comparing TLP do designs enhanced with TLP’s hardware budget (7KB)
  IPCP + 7KB —> Enhancing IPCP does not provide any improvements.
  Berti + 7KB —> Single-core: 0.0% | Multi-core: -3.6%
  Hermes + 7KB —> Single-core: 5.2% | Multi-core: 4.8%