## Slide 1: Enhancing Instruction Prefetching via Cache and TLB Management
Alexandre Valentin Jamet1, Georgios Vavouliotis2, Martí Torrents1,
Dimitrios Chasapis1, Marc Casas1
1Barcelona Supercomputing Center, 2Computing Systems Lab, Huawei Technologies AG, Switzerland
alexandre.jamet@bsc.es

## Slide 2: Executive Summary
Contemporary server workloads have massive instruction footprint
  Significant pressure on front-end structures
Mitigation techniques:
  L1i prefetching (e.g., FNL+MMA, Barça, EPI, FDiP)
  TLB prefetching (e.g., Morrigan)
  Prefetch-aware cache replacement policy (e.g., PACIPV, PACMAN)
Limitations in L1i page-cross prefetching mechanisms:
    Address translation latency becomes a bottleneck
    Insufficient utilization of lines brought by the L1i prefetcher in the L2C
Our approach
  Extend the sTLB with a buffer dedicated to translations brought by L1i prefetchers
  Adapt the L2C replacement to accommodate lines brought by L1i prefetchers
Notes: Quickly span through the problem of modern workloads (i.e., large data footprint).
Then, go on to explaining the different techniques available to workaround these problems:
Off-Chip Prediction (Predicting load demand accesses for cache hits)
Data Prefetching coupled with Adaptive Filtering (Improving prefetching for adaptive workload handling)
Cache bypassing (Selective bypass strategies for system performance)
Disruptive cache designs (Innovative architectures for efficiency and performance)

## Slide 3: Front-End Bottlenecks
Contemporary server workloads exhibit large instruction footprints
  Footprint growing by ~30% per year
  Front-end structures (i.e., L1i, TLBs) lag behind the demand of these workloads
More PTEs required to map the instruction footprint
L1i and sTLB misses dominate front-end stalls. Around 10% of total execution cycles in server workloads.
Notes: Here, we mention that modern workloads (and particularly GAP) put large load on the cache hierarchy.

## Slide 4: Impact of L1i Prefetching on TLBs
Cross-page prefetching consists in prefetching beyond page boundaries:
  An address translation might be needed.
[HPCA2025]: To Cross, or Not to Cross Pages for Prefetching?
Notes: Here, we mention that modern workloads (and particularly GAP) put large load on the cache hierarchy.

## Slide 5: Impact of L1i Prefetching on TLBs
Allowing instruction prefetchs to cross page boundaries delivers higher performance
The ideal scenario deliver even higher performance
Addressing the cost of address translation for these prefetches can deliver additional performance.
Notes: Here, we mention that modern workloads (and particularly GAP) put large load on the cache hierarchy.

## Slide 6: Impact of L1i Prefetching on L2C Management
We show that code lines brought by both in-page and cross-page prefetch requests incur pressure on the L2C;
Appropriate management of code lines has significant performance potential.
Adequate management of all lines brought by L1i prefetch requests shows higher benefits.
Notes: Here, we mention that modern workloads (and particularly GAP) put large load on the cache hierarchy.

## Slide 7: Reuse of Prefetched Code Lines
We analyze the reuse of code lines in the L2C;
A significant portion of codes lines brought by L1i Prefetch are dead on arrival;
Other lines experience a significant amount of reuse before eviction.
Lines brought by L1i prefetches experience variable reuse patterns and call for a smart policy.
Notes: Here, we mention that modern workloads (and particularly GAP) put large load on the cache hierarchy.

## Slide 8: IP-CaT: A Framework to coordinate instruction prefetching
Mitigating prefetch address translation costs yields higher performance:
  We introduce the tPB to optimize cross-page translations.
L1i prefetches exhibit variable reuse, requiring an intelligent policy:
  We propose TIPRP to manage L2C code lines via a variation of set-dueling
We combine tPB and TIPRP in a single proposal: IP-CaT.
tPB
TIPRP
Notes: Here we summarise the findings to transition to the design proposal.

## Slide 9: tPB: Accelerating Address Translation for Cross-Page Instruction Prefetches
The tPB is a 64-entry buffer for cross-page prefetch translations;
(1) tPB is looked up upon a miss in iTLB and STLB:
  (2) tPB hit, the entry is inserted in the sTLB;
  (3) tPB miss, a page table walk fills the tPB, which then updates the iTLB.

## Slide 10: TIPRP: Smart Management of L2C Instruction Lines
TIPRP is made of three sub-policies:
  PIP —> Prioritizes lines brought by L1i prefetch requests
  NPIP —> Deprioritizes lines brought by L1i prefetch requests;
  BIP —> Lines brought by L1i prefetch requests bypass the L2C;
The L2C is managed using a variation of set-dueling:
  Each sub-policy is applied in separate sets and competes to determine which is the best at a given time
  Events signaling a positive/negative behaviour for lines brought by L1i prefetch requests update PSEL1 and PSEL2
  Decision tree is designed to provide a continuum of policies

## Slide 11: IP-CaT: Synergistic TLB and Instruction Cache Management
The iTLB is looked up upon an L1i prefetch request
  iTLB miss —> STLB miss —> tPB look up
Upon a tPB miss, a page walk is initiated
  Address translation stored in iTLB and tPB when linked to an L1i cross-page prefetch request
  Otherwise, stored in iTLB and STLB
Upon a tPB hit, the entry is inserted in the STLB
TIPRP decides which sub-policy to enable in the following sets of the L2C
  c.f., TIPRP component

## Slide 12: Experimental Setup
ChampSim simulator (GitHub)
Considered µ-architectures:
  Cascade Lake
  Zen 4
Workloads
  Qualcomm & Server (105 workloads)
  SimPoints methodology
Single-core evaluation
Multi-page size evaluation
Multi-core evaluation
Component | Parameters | Latency
ITLB | 64-entry, 4-way | 1cc
DTLB | 64-entry, 4-way | 1cc
STLB | 3584-entry, 14-way | 8cc
L1 I-Cache | 32KB, 8-way | 4cc
L1 D-Cache | 32KB, 8-way, Berti Prefetcher | 4cc
L2 Cache | 1MB, 8-way | 10cc
LLC | 4MB/core, 8-way | 20cc
DRAM | 4GB, tRP=tRCD=tCAS=24cc | variable
*Representative of a Zen4 µ-arch.
Notes: Here, we simply describe the simulation set-up.

## Slide 13: Alternative Techniques
Designs evaluated:
  CHiRP
  Morrigan
  CLIP
  EMISSARY
  PACIPV
  PACMAN
  SRRIP (L2C)
  DRRIP
  SHiP++
  Mockingjay
  IP-CaT (our design)
Considered L1i Prefetchers:
  EPI
  FNL+MMA
  Barça
Notes: The alternative techniques we are considering.

## Slide 14: Single-Core Evaluation | Performance
Considering EPI in a single-core scenario, IP-CaT outperforms all evaluated designs
  TIPRP leverages 2.9% geomean speed-up
  IP-CaT (tPB+TIPRP) leverages 6.1% geomean speed-up

## Slide 15: Multi-Page Size Evaluation | Performance
We evaluate scenarios where 0%, 70%, 80%, 90%, and 100% of the memory footprint is mapped to large pages;
In all considered scenarios, IP-CaT outperforms all considered designs:
  When using more large pages, TIPRP provides most of the performance improvements;
  Trends are similar considering other L1i prefetcher (i.e., Barça, and FNL+MMA).

## Slide 16: Multi-Core Evaluation | Performance
We evaluate IP-CaT against other techniques in a 4-core scenario:
  In all considered scenarios, IP-CaT outperforms all considered designs

## Slide 17: Conclusions
We show that the address translation latency of L1i cross-page prefetch requests undermines the benefits of these prefetchers.
We propose the first work to orchestrate TLB and cache management to maximize the benefits of L1i prefetchers.
This work generalises to any L1i prefetchers.

## Slide 18: Thank you for your attention!
Enhancing Instruction Prefetching via Cache and TLB Management — ISCA’26
Paper available here:

## Slide 19: Acknoledgments/ Fundings
Alexandre Valentin Jamet acknowledges his AI4S fellowship within the “Generación D” initiative by Red.es, Ministerio para la Transformación Digital y de la Función Pública, for talent attraction (C005/24-ED CV1), funded by NextGenerationEU through PRTR.